## Slide 1
V5R2
V1R1
Yang Lei (Employee ID: wx491993)
Feb 01, 2019

## Slide 2: Storage Virtualization Basics

## Slide 3
Data has become an enterprise’s most important asset. How is data stored on the cloud? How is this different from the way it is stored with traditional IT? This chapter will answer these questions.

## Slide 4
Upon completion of this course, you will:
  Understand Huawei’s FusionSphere virtualization solution.
  Understand the storage architecture used for virtualized environments.
  Understand different types of disks.
  Understand the differences between centralized and distributed storage.
  Understand the differences between virtualized and non-virtualized storage.
  Understand different types of VM disks.
  Understand the storage features of Huawei’s virtualization product.

## Slide 5
Storage Architecture for Virtualization
Physical Disk Types and Related Techniques
Centralized Storage vs. Distributed Storage
Virtualized Storage vs. Non-Virtualized Storage
Introduction to VM Disks
Storage Features of Huawei’s Virtualization Product

## Slide 6: Where Do the Storage Resources Used by VMs Come From?
How do VMs access the underlying storage resources?
?
?

## Slide 7: Storage Architecture for Virtualization
Shared Catalog
qcow
raw
vmdk
vhd
others
Virtualized storage
NAS
Storage
Storage
Pool
File System
SAN
Storage
Storage
Pool
Logical Division
Logical
Volumes
File System
Distributed
Storage Pool
Logical Division
Logical Division
Distributed
Storage
Non-virtualized storage

## Slide 8: Virtualized Storage Conversion Path in Cloud Computing
Physical
volume
RAID or Replication
Physical
volume
Logical division
Logical
volume
Format
NFS file
system
Attach to compute cluster and format
Virtual file
system
Shared Catalog
Shared Catalog
Notes: 本页胶片在《虚拟化存储与非虚拟化存储》也有，讲师可根据实际情况或个人习惯，选择先将此页胶片展示给学员，然后在后面小节中详细讲解，或者隐藏此页。
This slide also appears in “Virtualized Storage vs Non-Virtualized Storage”. The lecturer can choose to show or hide this slide at his or her discretion.

## Slide 9: Non-Virtualized Storage Conversion Path in Cloud Computing
Physical
volume
RAID or Replication
Logical division
Logical
volume
Attach to compute cluster
Notes: 和上页一样，本页胶片在《虚拟化存储与非虚拟化存储》也有，讲师可根据实际情况或个人习惯，选择先将此页胶片展示给学员，然后在后面小节中详细讲解，或者隐藏此页。
This slide also appears in “Virtualized Storage vs Non-Virtualized Storage”. The lecturer can choose to show or hide this slide at his or her discretion.

## Slide 10
Storage Architecture for Virtualization
Physical Disk Types and Related Techniques
Centralized Storage vs. Distributed Storage
Virtualized Storage vs. Non-Virtualized Storage
Introduction to VM Disks
Storage Features of Huawei’s Virtualization Product

## Slide 11: Physical Disk Type - SATA
SATA (Serial Advanced Technology Attachment), also called serial ATA, is a computer bus interface that connects host bus adapters to mass storage devices. Using serial communication, the serial ATA bus uses embedded clock signals to check transmission commands (not only data) and automatically corrects detected errors, ensuring reliable data transmission for SATA disks. The SATA interface is simple and the disks are hot-swappable.

## Slide 12: Physical Disk Type - SAS
Serial Attached SCSI (SAS) is a new-generation SCSI technology, which, like the popular Serial ATA (SATA), also uses serial communication to achieve a higher transmission speed. Compared with the older parallel SCSI, SAS improves the efficiency, availability, and scalability of storage systems and offers optional compatibility with SATA.

## Slide 13: Physical Disk Type - NL-SAS
Nearline SAS (NL-SAS) disks are a combination of a SAS interface with SATA disks. The rotational speed of NL-SAS disks is only 7200 rpm, so performance is lower than that of SAS disks. However, with the SAS interface, addressing and speed are improved.

## Slide 14: Physical Disk Type - SSD
A solid-state drive (SSD) is a solid-state storage device that uses integrated circuit assemblies as non-volatile memory. An SSD consists of a control unit and a storage unit (flash or DRAM chip). An SSD is the same as a common hard disk drive (HDD) in terms of interface specifications and definition, functionality, usage, and product shape and size. Although SSDs deliver fast read/write performance, light weight, low power consumption, and compact sizes which traditional HDDs cannot rival, SSDs have a shorter lifespan and higher price.

## Slide 15: Comparing Different Types of Physical Disks
Performance
Price

## Slide 16
Storage Architecture for Virtualization
Physical Disk Types and Related Techniques
Centralized Storage vs. Distributed Storage
Virtualized Storage vs. Non-Virtualized Storage
Introduction to VM Disks
Storage Features of Huawei’s Virtualization Product

## Slide 17: Centralized Storage
Storage
Pool
RAID
Data read/write
Data read/write
Data read/write
Data read/write

## Slide 18: RAID Technology
2
1
Parallel read and write on multiple disks
Efficient
Parity check and hot backup
Safe
RAID

## Slide 19: Common RAID Types
D0
D1
D2
D3
D4
D0
D2
D4
D1
D3
D5
D0, D1, D2, D3, D4, D5
Disk 1
Disk 2
D5
Logical Disks
D0
D1
D0
D1
D2
D0
D1
D2
D0, D1, D2
Disk 1
Disk 2
D2
Logical Disks
D0
D1
D0
D2
P2
D1
P1
D4
D0, D1, D2, D3, D4, D5
Disk 1
Disk 2
Logical Disks
P0
D3
D5
Disk 3
P0
D2
P1
D3
P2
D4
D5
D0
D1
D0
D2
P2
D1
P1
Q2
D0, D1, D2, D3, D4, D5, D6, D7
Disk 1
Disk 2
P0
Q1
D4
Disk 3
P0
Q0
D3
D5
Disk 4
Q3
D6
D7
P3
Q0
D2
P1
Q1
D3
P2
Q2
D4
D5
Q3
D6
D7
P3
RAID 0
RAID 1
RAID 5
RAID 6

## Slide 20: Centralized Storage Types
IP/FC network
Windows
client
Unix-like
client
Windows server
Unix-like
server
NAS
CIFS
NFS
SAN
NAS

## Slide 21: IP SAN & FC SAN
IP SAN is a storage area network architecture that is built on Ethernet and uses TCP/IP as the underlying transport protocol. The typical protocol that implements IP SAN is iSCSI. It defines how SCSI instruction sets are encapsulated during IP transmission.
Storage device
Storage device
Ethernet switch
Server
User B
Server
User C
User A
LAN
TCP/IP network
iSCSI
Storage device
Storage device
FC switch
Server
User B
Server
User C
User A
LAN
FC network
FC
Servers and storage devices are directly connected through FC switches.

## Slide 22: IP SAN vs FC SAN
Description | IP SAN | FC SAN
Network speed | 1 Gbit/s, 10 Gbit/s, 40 Gbit/s | 4 Gbit/s, 8 Gbit/s, 16 Gbit/s
Network architecture | Existing IP networks | Dedicated FC network and HBA card
Transmission distance | No limit in theory | Limited by the transmission distances of optical fibers
Management and maintenance | Simple operations like those with IP devices | Complex techniques and management
Compatibility | Compatible with all IP network devices | Poor compatibility
Performance | 1 Gbit/s is the current mainstream; 10 Gbit/s is emerging. | High transmission and read/write performance
Cost | Low purchase and maintenance costs | High purchase costs (FC switches, HBA cards, FC disk arrays, etc.) and maintenance costs (personnel training, system configuration and monitoring)
DR | Built-in local and remote disaster recovery capability at low costs | High hardware and software costs for DR
Security | Relatively low | High

## Slide 23: NAS Architecture
LUN0
LUN1
LUN2
LUN3
LUN6
LUN7
LUN8
LUN9
LUN4
LUN5
LUN11
Volume Management Module
Volume Management Module
File System
Network file system protocol (NFS/CIFS)
Ethernet Interface
Ethernet Interface
LUN10

## Slide 24: CIFS
Common Internet File System (CIFS) is a shared open file system developed from Microsoft’s Server Message Block (SMB). In a Windows OS, you can mount shared resources on the CIFS server to your own system by creating a simple shared mapping. Then you can use the shared resources as if using local resources.

## Slide 25: NFS
Network File System (NFS) was originally developed by Sun Microsystems. It can be used for cross-network file sharing in UNIX-like operating systems such as Linux/UNIX/AIX/HP-UX/Mac OS X. You can use the mount command to mount remote file systems to your own file system, and access the remote shared files as if accessing local files.

## Slide 26: CIFS vs NFS
 | CIFS | NFS
Transmission | Network-based, high reliability requirements | Transmission-independent
Ease of use | No additional software required | Dedicated software required
Security | No error correction | Error correction supported
File conversion | No file format retained. | File format retained

## Slide 27: Distributed Storage
Distributed
Storage
Pool
Replication
Data read/write
Data read/write
Data read/write
Data read/write

## Slide 28: Replication
Distributed
Storage Pool
Data write

## Slide 29: Replication
Distributed
Storage Pool
Distributed
Storage Pool
Data write
Data read

## Slide 30: Popular Distributed Storage Products

## Slide 31
Storage Architecture for Virtualization
Physical Disk Types and Related Techniques
Centralized Storage vs. Distributed Storage
Virtualized Storage vs. Non-Virtualized Storage
Introduction to VM Disks
Storage Features of Huawei’s Virtualization Product

## Slide 32: Virtualized Storage Conversion Path in Cloud Computing
Physical
volume
RAID or Replication
Physical
volume
Logical division
Logical
volume
Format
NFS file
system
Attach to compute cluster and format
Virtual file
system
Shared Catalog
Shared Catalog

## Slide 33: Non-Virtualized Storage Conversion Path in Cloud Computing
Physical
volume
RAID or Replication
Logical division
Logical
volume
Attach to compute cluster

## Slide 34: Relationship Between RAIDs and LUNs
A RAID array can be seen as a large physical volume made up of a number of hard disks.
On top of a physical volume, you can create one or more logical units of specified capacities. These logical units are called Logical Unit Numbers (LUNs) and can be mapped to hosts as basic block devices.
Physical volume
Physical volume
Logical volume
Logical volume
Create one logical volume on a single physical volume
Create multiple logical volumes on a single physical volume
LUN 1
LUN 2
LUN 3

## Slide 35: Process of Creating a LUN
LUN 1
LUN 2
LUN 3
Segmentation
Logical volume
Physical volume
Hard disk
RAID
Logical division

## Slide 36: Pool & Volume & LUN
A storage pool is a container of storage resources. The storage resources used by application servers all come from storage pools.
A volume is an internal object managed inside a storage system.
A LUN is a storage unit that can be directly mapped to a host for data read and write. It is how volumes are provisioned to application servers.
Volume
LUN
Server
Pool

## Slide 37: Common File Systems
Virtual clustered file system
NAS file system
File system in an OS

## Slide 38: Mapping a File to a Disk
User
File
File system
File system blocks
Logical locations of LVM
Physical locations on disks
Disk sectors
Create
Store
Mapping via file system
Mapping
Mapping via LVM
Mapping

## Slide 39
Storage Architecture for Virtualization
Physical Disk Types and Related Techniques
Centralized Storage vs. Distributed Storage
Virtualized Storage vs. Non-Virtualized Storage
Introduction to VM Disks
Storage Features of Huawei’s Virtualization Product

## Slide 40: VM Disks
User view
Administrator view
Notes: 虚拟机磁盘是文件系统上的一个文件，对于一个客户操作系统而言，就好像是一个物理磁盘驱动器。这个文件既可以在主机上，也可以在一个远端文件系统上。在给虚拟机配置虚拟磁盘后，可以安装一个新的操作系统到该磁盘文件。

## Slide 41: Common VM Disk Formats
VM Disk File Format | Vendor
RAW | All
VMDK | VMware
VHD | Microsoft Hyper-V, Huawei FusionCompute
QCOW | QEMU or KVM virtualization platforms only
QED | 
VDI | Oracle

## Slide 42
Storage Architecture for Virtualization
Physical Disk Types and Related Techniques
Centralized Storage vs. Distributed Storage
Virtualized Storage vs. Non-Virtualized Storage
Introduction to VM Disks
Storage Features of Huawei’s Virtualization Product

## Slide 43: Storage Architecture for Huawei Virtualization Product
Data store
Storage device
Storage resource
SAN/NAS
LUN
Shared catalog
RDM
Virtualized storage
Non-virtualized storage
FusionStorage
Block

## Slide 44: Huawei Virtual Disk Features
Type
Common
Shared
Configuration Mode
Common
Thin-provision
Disk Mode
Dependent
Independent & persistent
Independent & nonpersistent
Multi-tenant sharing
Space-saving
Temporary data storage
Fast read/write
Customer needs

## Slide 45
At this point you should understand how data is written to storage devices in virtualization scenarios.

## Slide 46
Which of the following disk types is recommended for an archive room that needs to store large amounts of data that will be accessed infrequently over long periods of time? ( )
  A. SSD
  B. SAS disk
  C. SATA disk
  D. NL-SAS disk
SATA disks use a parallel interface while SAS disks use a serial interface.
  A. TRUE
  B. FALSE
Notes: 参考答案：

## Slide 47
Huawei e-Learning website
  http://support.huawei.com/learning/Index!toTrainIndex
Huawei Support case library
  http://support.huawei.com/enterprise/servicecenter?lang=en
HCIA-Cloud Computing v4.0 online forum
  https://forum.huawei.com/enterprise/en/Huawei-Official-Communication-Channel-HCNA-Cloud-Certification-Course/thread/456287-911